INFORMATION SHEET

NO. FS-05

DATE	:	April 13, 2015

CATEGORY	:	Fire Safety

SUBJECT		:	Sprinkler Systems Requirements for Addition or Legalization of 				Dwelling Unit

PURPOSE        	:     The purpose of this Information Sheet is to clarify the sprinkler systems requirements for addition or legalization of dwelling unit.

REFERENCE    	:     2013 San Francisco Building Code

Ordinance No. 43-14

Ordinance No. 49-14

Ordinance No. 30-15

DISCUSSION		:  	The requirements for sprinkler systems for addition or legalization of dwelling unit.

- When the occupancy is changed from Group R3 to Group R2 by adding or legalizing a dwelling unit, resulting in a building not more than 3 stories and within existing building envelope:

- If the added or legalized dwelling unit is on the first floor,

- Sprinklers will be required on the entire first level designed per designated hazard classification (NFPA 13R and NFPA 13); and,

- For building more than 2 stories, the first floor shall be separated from the upper floor by 2-hour fire rated construction applied on the affected side.

- If the added or legalized dwelling unit is not located on the first floors,

- Sprinklers  will be required for the added or legalized dwelling unit and the egress path of the unit; and,

- For buildings more than 2 stories, the first floor shall be separated from the upper floor by 2-hour fire rated construction applied on the affected side.

- When the occupancy is changed from Group R3 to Group R2 by adding or legalizing a dwelling unit, resulting in a building more than 3 stories:

- If building envelope is changed (excluding exterior egress), the entire building needs to be fully sprinklered.

- If story count is increased to 4 stories within existing envelope, entire building shall be sprinklered.

- If story count is not changed and within existing envelope, sprinklers will be required for the added or legalized dwelling unit and the egress path of that unit.

- When a dwelling unit is added or legalized in a Group R2 building within existing building envelope, sprinklers will only be required for the added or legalized dwelling unit and the egress path of that unit.

- In an existing 3- or 4-story building or building which is increased to resulting in 3- or 4-story, the ground floor ceiling may be upgraded to 2-hour rated construction in lieu of upgrading to 1-hour rated building.

- This Information Sheet is applicable to any of the following:

- Ordinance No. 43-14: Legalization of Dwelling Units Installed Without A Permit

- Ordinance No. 49-14: Construction of In-Law Units in Existing Residential Buildings of Auxiliary Structures on the Same Lot; Rent Control

- Ordinance No. 30-15: Adding Dwelling Units to Existing Buildings Undergoing Seismic Retrofitting

OTHER CONDITIONS:

Other conditions will be evaluated on a case-by-case basis by the Supervisor or Manager.

Pre-application meeting or approval of AB-005 is required.

______________________________________________

Michie Wong		Date

Fire Marshall & Assistant Deputy Chief

San Francisco Fire Department

______________________________________________

Tom C. Hui, S.E., C.B.O.		Date

Director

Department of Building Inspection

# Text boxes

This Information Sheet is subject to modification at any time. For the most current version, visit our website at http://www.sfdbi.org