INFORMATION SHEET

NO. S-17

DATE	:	August 16, 2017

SUBJECT	:	Structural

TITLE	:	Anchor Channels in Concrete Elements

REFERENCE	:	San Francisco Building Code (SFBC) Section 19 or 35

AC232 by ICC-ES

Information Sheet No. G-21: Products Acceptance

PURPOSE	:	To establish criteria for acceptance of products used as Anchor Channels in Concrete Elements

DISCUSSION	: 	The following products for construction are acceptable:

- Products with a current ICC-ES report by ICC (International Code Council) Evaluation Service tested in accordance with AC232 that include approvals for seismic design categories A through F and loading in all three principal direction (tension Nua, shear Vua,y, and longitudinal Vua,x); Evaluation Reports link: http://www.icc-es.org/Evaluation_Reports/

Other conditions will be evaluated on a case-by-case basis by the Supervisor or Manager.

_________________________________________________

Tom C. Hui, S.E., C.B.O.			Date

Director

Department of Building Inspection

# Text boxes

This Information Sheet is subject to modification at any time. For the most current version, visit our website at http://www.sfdbi.org